## Slide 1: Another Trellis Example
ECE111
Term Project

## Slide 2: Sample Trellis: note bad bit @x=4
blue squares = states
numbers in blue squares = cumulative error count

## Slide 3: Note error counts in each column
 | 0 | 1 | 2 | 3 | 4* | 5 | 6 | 7 | 8
 | 0 | 0 | 2 | 3 | 4 | 2 | 3 | 3 | 1
 | 0 | 2 | 0 | 3 | 3 | 4 | 3 | 3 | 3
 | 0 | 0 | 3 | 1 | 4 | 4 | 1 | 4 | 4
 | 0 | 0 | 3 | 0 | 4 | 4 | 3 | 4 | 4
 | 0 | 0 | 0 | 4 | 2 | 3 | 3 | 1 | 4
 | 0 | 0 | 0 | 4 | 3 | 1 | 3 | 3 | 4
 | 0 | 0 | 0 | 3 | 1 | 2 | 4 | 3 | 3
 | 0 | 0 | 0 | 5 | 1 | 2 | 2 | 3 | 4
Step 3: Still one perfect path (Hamming separation of 0)
Step 4: Two best paths have 1 error each (Hamming separation of 1)
Step 5: Down to one best path with 1 bit error
Step 8: Obvious winner -- score 1 because of error at step 4

## Slide 4: What was the most likely original data sequence?
Reconstructed original sequence =
000 0 1 1 0 1 0 0 0
Run sim of our HW7 with 'o17 and 'o13
Note: Their shift reg runs right to left, which is why I reversed 4'o15 into 4'o13. I also reversed the order of the two tap patterns to match their nomenclature.
Note that our best (lowest-error) path has 1 error, consistent with the single bad bit that was injected.

## Slide 5: Efficient Viterbi Decoder Architecture Traceback Procedure
1. Initialize Data Structures
1.1. Initialize the trellis stage pointer to zero. Initialize the path memory write pointer to zero. Initialize the traceback pointer to zero. Initialize the decoded symbol counter to zero.
1.2. Initialize the path metric for the known initial state to zero, with the remaining 2M â€“1 path metrics to their maximum value. Go to step 2.

## Slide 6: 2. Compute Path Metrics and Survivors
2.1. Increment the trellis stage pointer and the path memory pointer.
2.2. For every trellis node, compute 2k path metrics by summing the path metrics from nodes at the previous stage to the corresponding branch metrics computed at the present stage.
2.3. Compare the 2k paths and select the path with the minimum path metric as the surviving path; all other incoming paths to the trellis node are no longer considered.
If there is a tie between path metrics, select one path arbitrarily.

## Slide 7: 2. Compute Path Metrics and Survivors
2.4. Store the path metric. Update the surviving path by shifting in the surviving backward label to the left hand side of the path memory register where the surviving path currently terminates.
2.5. If the path memory write pointer is < T then go to step 2.1, else if the path memory write pointer = T go to step 3

## Slide 8: 3. Traceback and Output Decision
3.1. Set traceback pointer to T.
Traceback start state number = state with smallest path metric.
3.2. Combine state number and traceback pointer into a row-column address used to index path memory.
Use this to read a backward label from path memory.
Determine a predecessor state on the surviving path from the traceback mapping function.
Decrement the traceback pointer.
If the traceback pointer >1 repeat step 3.2, else go to step 3.3

## Slide 9: 3. Traceback and Output Decision
3.3. Produce a decoded symbol.
3.3.1. Category 1 - A decoder decision is made for one symbol by selecting the rightmost elements of the traceback mapping register. 3.3.2. Category 2 - A decoder decision is made for one symbol by selecting a combination of specific elements from the backward label read from path memory and the rightmost elements of the traceback mapping register4.
3.4. Increment the decoded symbol counter. If the decoded symbol count < N, go to step 2.1, else finish.|