## Slide 1: Convolutional Encoding Viterbi Decoding
WES269 Winter 2022
Lecture 2

## Slide 2: Interesting quote of the day
"First, computer software and hardware are the most complex and rapidly developing intellectual creations of modem man."
-- p. iii, Internet and Computer Law, P. B. Maggs, J. T. Soma, and J. A. Sprowl, 2001
... but you already knew that :)

## Slide 3: Credits: Today’s lecture is based on:
A Tutorial on Convolutional Coding with Viterbi Decoding
Chip Fleming
Spectrum Applications

## Slide 4: Origin of Viterbi Decoding
Andrew J. Viterbi, "Error Bounds for Convolutional Codes and an Asymptotically Optimum Decoding Algorithm," IEEE Transactions on Information Theory, Volume IT-13, pp. 260-269, April 1967.
Viterbi is a founder of Qualcomm.

## Slide 5: Terminology
k number of message symbols
n number of codeword symbols
r rate = k/n
m number of encoding cycles an input symbol is stored
K number of input symbols used by encoder to compute each output symbol (decoding time exponentially dependent on K)

## Slide 6: Convolutional Encoder
flip flop
(stores one bit)
n = 2*k, r = ½, K = 3, m = 2 (why?)
output upper input
followed by lower input

## Slide 7: Encoding Example
Input: 010111001010001
Output: 00 11 10 00 01 10 01 11 11 10 00 10 11 00 11
Both flip flops set to 0 initially.
Flush encoder by clocking m = 2 times with 0 inputs.
FFs are dly[1] and dly[2] in my simulation

## Slide 8: insert Verilog/ModelSim demo here
Note 2:1 rate change
Suitable for QPSK, for example
Show 2 versions of ModelSim:
  one bit in, two bits out at CLK rate
  one bit out at CLK rate, one bit in every 2 clocks
  both produce the same result
Now let's decode

## Slide 9: decode content
Viterbi decoding for convolutional codes
Hidden Markov models
The hidden model is the transmitter's convolutional encoder and its uncorrupted data stream.
We are trying to revers-engineer this sequence by observing a possibly corrupted version of the transmitted data stream.
With contributions taken from Dan Durafsky

## Slide 10: Problem formulation
noise
information
Finite State Machine
observation
What is the best estimate for the information given the observation?
Maximum Likelihood receiver:
max P( Y | X ) = max P( X+N | X ) = max P( N )
for independent transmissions = max i=1,L P( Ni )
 minimum weight noise sequence
x
n
y = x + n

## Slide 11: The Noisy Channel Model
Search through space of all possible sentences.
  uh ... that's a kinda big space ...
Pick the one that is most probably the given the waveform.

## Slide 12: characteristics
Viterbi algorithm ("VA" block) common in high-speed modems.
key building block of modern information infrastructure
Summary:
VA finds a path through any Markov graph
M. graph = sequence of states governed by a Markov chain.
Sample practical applications:
  convolutional decoding and channel trellis decoding.
  fading communication channels,
  partial response channels in recording systems,
  optical character recognition,
  voice recognition.
  DNA sequence analysis

## Slide 13: Illustration of the algorithm
st 1 0.7 st 2
0.5 0.2
IEM 0.5 1.2 UNI
0.8 0.2
st 3 st 4
0.8
0.5
1.2
1.2
1.0
0.8
survivor
Walk through states (st *). Figure of merit = low diff. = high correlation between
observed data and data output stream from each sequence of states.

## Slide 14: Key idea
Best path from A to C = best of
- the path A-F-C
- best path A to B + best path from B to C
- the path via D does not influence the best way from B to C
A
B
C
D
E
F

## Slide 15: Application to convolutional code
encoder
VD
channel
Info code code + noise estimate
binary noise sequences
P(n1=1)=P(n2=1) = p
I
delay
c1
c2
n1
n2
c1 n1
c2 n2
find sequence I‘ that corresponds to code sequence ( c1, c2 ) at minimum distance from (r1,r2) = (c1  n1, c2  n2)

## Slide 16: Use encoder state space
I
delay
c2
00
01
11
10
State 0
State 1
Time 0 1 2 3
00
01
11
10
00
01
11
10
00
01
11
10
•••

## Slide 17
00
11
State 0
State 1
00
01
11
10
00
01
11
10
00
01
11
10
•••
00
11
State 0
State 1
00
01
11
10
00
01
11
10
00
01
11
10
•••
Encoder output 00 11 10 00
channel output 00 10 10 00
0
2
1
1
1
2
1
3
best

## Slide 18: Viterbi Decoder action
Maximum Likelihood receiver: find ( c1, c2 ) that maximizes
Probability ( r1, r2 | c1, c2 ) = Prob ( c1  n1, c2  n2 | c1, c2 ) =
= Prob ( n1, n2 )
= minimum # noise digits equal to 1

## Slide 19: Distance Properties of Conv. Codes
Def: The free distance, dfree, = minimum Hamming distance between any two code sequences.
Criteria for good convolutional codes:
  1. Large free distance, dfree.
  2. Small numer of information bits = 1 in sequences with low Hamming weight
There is no known constructive way of designing a convolutional code of given distance properties.
However, a given code can be analyzed to find its distance properties.

## Slide 20: Distance Prop. of Convolutional Codes (cont’d)
Convolutional Codes 20
Convolutional codes are linear =>
Hamming distance between any two code sequences corresponds to the Hamming distance between the all-zero code sequence and any nonzero code sequence.
The nonzero sequence of minimum Hamming weight diverges from the all-zero path at some point and remerges with the all-zero path at some later point.

## Slide 21: Distance Properties: Illustration
sequence 2: Hamming weight = 5, dinf = 1
sequence 3: Hamming weight = 7, dinf = 3.
seq 2: one wrong move
seq 3: three wrong moves

## Slide 22: Modified State Diagram (cont’d)
Path from (00) to (00) is denoted by
Di (weight)
Lj (length)
Nk (# info 1‘s)

## Slide 23: Transfer Function
The transfer function T(D,L,N)

## Slide 24: Transfer Function (cont’d)
Performing long division:
  T(D,L,N) = D5L3N + D6L4N2 + D6L5N2 + D7L5N3 + ….
If want Hamming distance of the code only,
set N = 1 and L = 1 to get the distance transfer function:
  T (D) = D5 + 2D6 + 4D7 + …
  There is one code sequence of weight 5. Therefore dfree=5.
  There are two code sequences of weight 6,
  four code sequences of weight 7, ….

## Slide 25
red = no FEC; blue = hard decision Viterbi; green = soft decision Viterbi
This is for a
common (171,133)
trellis
Note bit error rate = 5*10-1 is as bad as it gets

## Slide 26
(001)(111)(001) = 171 octal
(001)(011)(011) = 133 octal
Same rate as our earlier 3-tap example

## Slide 27
So why the longer constraint length?
It's cheap enough at the encoder, but a pain in the decoder.
Longer constraint length => greater potential distance between output sequences.
A given error or group of errors is less likely to be mis-corrected.

## Slide 28: performance
The event error probability = probability that the decoder selects a code sequence that was not transmitted
For two codewords the Pairwise Error Probability is
The upperbound for the event error probability is given by
correct
node
incorrect

## Slide 29: performance
using the T(D,N,L), formulate this as
The bit error rate (not probability) is

## Slide 30
The constraint length of the ½ convolutional code: k = 1 + # memory elements
Complexity Viterbi decoding: proportional to 2K (number of different states)

## Slide 31
Note with any error correction scheme there is a minimum Eb/No, below which the error "correction" scheme may make things worse.
Simulink demo

## Slide 32
PERFORMANCE:
theoretical uncoded BER given by
where Eb is the energy per information bit
for the uncoded channel, Es/N0 = Eb/N0, since there is one channel symbol per bit.
for the coded channel with rate k/n, nEs = kEb and thus Es = Eb k/n
The loss in the signal to noise ratio is thus -10log10 k/n dB
rate ½ codes => lose 3 dB SNR at the receiver

## Slide 33: metric (not Imperial or English :) )
We determine the Hamming distance between the received symbols and the code symbols
d(x, y) = metric
Properties:
d(x, y) ≥ 0 (non-negativity)
d(x, y) = 0 if and only if x = y (identity)
d(x, y) = d(y, x) (symmetry)
d(x, z) ≤ d(x, y) + d(y, z) (triangle inequality).

## Slide 34: Markov model for Dow Jones (stock prices)
Figure from Huang et al, via

## Slide 35: Markov Model for Dow Jones
What is the probability of 5 consecutive up days?
Sequence is up-up-up-up-up
I.e., state sequence is 1-1-1-1-1
P(1,1,1,1,1) =
  1a11a11a11a11 = 0.5 x (0.6)4 = 0.0648

## Slide 36: Application to Hidden Markov Models
Definition of HMM: inite set of states, each of which is associated with a probability distribution.
transitions among the states are governed by a set of probabilities called transition probabilities. ome or observation can be generated, according to the associated probability distribution.
Only the outcome, not the state, is visible to an external observer
States are ``hidden'' to the outside; hence the name Hidden Markov Model.
EXAMPLE APPLICATION: speech recognition and synthesis

## Slide 37: Example HMM for Dow Jones (from Huang et al.)
1
2
3
0.2
0.5
0.2
0.1
0.3
0.6
0.5
0.2
0.4
P(up)
P(down) =
P(no-change)
0.3
0.3
0.4
0.7
0.1
0.2
0.1
0.6
0.3
0.5
0.2 = initial state probability
0.3
0.6
0.5
0.4
0.2
0.3
0.1
0.2
0.2 transition matrix
0.5

## Slide 38: Calculate Probability ( observation | model )
Trellis:
0.5
0.3
0.2
P(up)
P(down)
P(no-change)
0.3
0.3
0.4
0.7
0.1
0.2
0.1
0.6
0.3
0.179
0.036
0.008
Probability, UP, UP, UP, ***
0.35
0.02
0.09
0.35*0.2*0.3
0.02*0.5*0.7
0.09*0.4*0.7
0.02*0.2*0.3
0.09*0.5*0.3
0.35*0.6*0.7
0.179*0.6*0.7
0.008*0.5*0.7
0.036*0.4*0.7
0.6
0.5
0.4
0.2
0.3
0.1
0.2
0.2 transition matrix
0.5
0.223
0.46
add probabilities !

## Slide 39: Calculate Probability ( observation | model )
Note: The given algorithm calculates

## Slide 40: Calculate maxS Prob( up, up, up and state sequence S )
0.35
0.09
0.02
P(up)
P(down)
P(no-change)
0.3
0.3
0.4
0.7
0.1
0.2
0.1
0.6
0.3
0.147
0.021
0.007
Observation is (UP, UP, UP, *** )
0.35*0.2*0.3
0.02*0.5*0.7
0.09*0.4*0.7
0.02*0.2*0.3
0.09*0.5*0.3
0.35*0.6*0.7
0.147*0.6*0.7
0.007*0.5*0.7
0.021*0.4*0.7
0.6
0.5
0.4
0.2
0.3
0.1
0.2
0.2 transition matrix
0.5
0.5
0.2
0.3
best
Select highest probability !

## Slide 41: Calculate maxS Prob( up, up, up and state sequence S )
Note: The given algorithm calculates
Hence, we find
the most likely state sequence given the observation

## Slide 42
06 June 2005 08:00 AM (GMT -05:00)
Send Link
Printer Friendly
(From The Institute print edition) Viterbi Receives Franklin Medal
As a youth, Life Fellow Andrew Viterbi never envisioned that he’d create an algorithm used in every cellphone or that he would cofound Qualcomm, a Fortune 500 company that is a worldwide leader in wireless technology.
Viterbi came up with the idea for that algorithm while he was an engineering professor at the University of California at Los Angeles (UCLA) and then at the University of California at San Diego (UCSD), in the 1960s. Today, the algorithm is used in digital cellphones and satellite receivers to transmit messages so they won’t be lost in noise. The result is a clear undamaged message thanks to a process called error correction coding. This algorithm is currently used in most cellphones.
“The algorithm was originally created for improving communication from space by being able to operate with a weak signal but today it has a multitude of applications,” Viterbi says.
For the algorithm, which carries his name, he was awarded this year’s Benjamin Franklin Medal in electrical engineering by the Franklin Institute in Philadelphia, one of the United States’ oldest centers of science education and development. The institute serves the public through its museum, outreach programs, and curatorial work. The medal, which Viterbi received in April, recognizes individuals who have benefited humanity, advanced science, and deepened the understanding of the universe. It also honors contributions in life sciences, physics, earth and environmental sciences, and computer and cognitive sciences.
Qualcomm wasn’t the first company Viterbi started. In the late 1960s, he and some professors from UCLA and UCSD founded Linkabit, which developed a video scrambling system called Videocipher for the fledgling cable network Home Box Office. The Videocipher encrypts a video signal so hackers who haven’t paid for the HBO service can’t obtain it.
Viterbi, who immigrated to the United States as a four-year-old refugee from facist Italy, left Linkabit to help start Qualcomm in 1985. One of the company’s first successes was OmniTracs, a two-way satellite communication system used by truckers to communicate from the road with their home offices. The system involves signal processing and an antenna with a directional control that moves as the truck moves so the antenna always faces the satellite. OmniTracs today is the transportation industry’s largest satellite-based commercial mobile system.
Another successful venture for the company was the creation of code-division multiple access (CDMA), which was introduced commercially in 1995 in cellphones and is still big today. CDMA is a “spread-spectrum” technology—which means it allows many users to occupy the same time and frequency allocations in a band or space. It assigns unique codes to each communication to differentiate it from others in the same spectrum.
Although Viterbi retired from Qualcomm as vice chairman and chief technical officer in 2000, he still keeps busy as the president of the Viterbi Group, a private investment company specializing in imaging technologies and biotechnology. He’s also professor emeritus of electrical engineering systems at UCSD and distinguished visiting professor at Technion-Israel Institute of Technology in Technion City, Haifa. In March he and his wife donated US $52 million to the University of Southern California in Los Angeles, the largest amount the school ever received from a single donor.
To honor his generosity, USC renamed its engineering school the Andrew and Erna Viterbi School of Engineering. It is one of four in the nation to house two active National Science Foundation–supported engineering research centers: the Integrated Media Systems Center (which focuses on multimedia and Internet research) and the Biomimetic Research Center (which studies the use of technology to mimic biological systems).
Andrew Viterbi

## Slide 43: Viterbi Decoding Applications
decoding trellis-coded modulation in modems
most common FEC technique used in space communications (r = ½, K = 7)
usually implemented as serial concatenated (nested) block and convolutional coding – first Reed-Solomon, then convolutional; opposite order on decode
Turbo codes are a parallel-concatenated convolutional coding technique
  Use soft output Viterbi in feedback loop
  actually reasonably named

## Slide 44: State Transition and Output Tables
 | Next State, if | 
Current State | Input = 0: | Input = 1:
00 | 00 | 10
01 | 00 | 10
10 | 01 | 11
11 | 01 | 11
 | Output Symbols, if | 
Current State | Input = 0: | Input = 1:
00 | 00 | 11
01 | 11 | 00
10 | 10 | 01
11 | 01 | 10
State transition table
Output table
2m rows

## Slide 45: State Transitions
input symbol is 1
input symbol is 0
arcs labeled with output symbols

## Slide 46: Trellis

## Slide 47: Trellis and trajectory
Trellis repeats at every position
Trajectory goes upward for data input 0, downward for 1

## Slide 48: Oops! Errors in received bits!

## Slide 49: Viterbi Decoding - Accumulated Error Metric
(use Hamming distance in our example)
Trying to find the input sequence whose corresponding output matches the received output as closely as possible.

## Slide 50: Accumulated Error Metric

## Slide 51: Decoder Trellis

## Slide 52: Decoder Trellis

## Slide 53: Decoder Trellis

## Slide 54: So many paths, so little time
As you can easily see, there are may possible paths through the trellis, even though there are only four states and two possible data input values.
The key is in the pruning, retaining only the most promising paths and discarding the ones with the largest errors.

## Slide 55: Final Decoder Trellis

## Slide 56: Accumulated Error Metric over Time
t = | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
State 002 |  | 0 | 2 | 3 | 3 | 3 | 3 | 4 | 1 | 3 | 4 | 3 | 3 | 2 | 2 | 4 | 5 | 2
State 012 |  |  | 3 | 1 | 2 | 2 | 3 | 1 | 4 | 4 | 1 | 4 | 2 | 3 | 4 | 4 | 2 | 
State 102 |  | 2 | 0 | 2 | 1 | 3 | 3 | 4 | 3 | 1 | 4 | 1 | 4 | 3 | 3 | 2 |  | 
State 112 |  |  | 3 | 1 | 2 | 1 | 1 | 3 | 4 | 4 | 3 | 4 | 2 | 3 | 4 | 4 |  | 
Last two inputs known to be zero.

## Slide 57: Surviving Predecessor States
t = | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
State 002 | 00 | 00 | 00 | 01 | 00 | 01 | 01 | 00 | 01 | 00 | 00 | 01 | 00 | 01 | 00 | 00 | 00 | 01
State 012 | 00 | 00 | 10 | 10 | 11 | 11 | 10 | 11 | 11 | 10 | 10 | 11 | 10 | 11 | 10 | 10 | 10 | 00
State 102 | 00 | 00 | 00 | 00 | 01 | 01 | 01 | 00 | 01 | 00 | 00 | 01 | 01 | 00 | 01 | 00 | 00 | 00
State 112 | 00 | 00 | 10 | 10 | 11 | 10 | 11 | 10 | 11 | 10 | 10 | 11 | 10 | 11 | 10 | 10 | 00 | 00

## Slide 58: States Selected when Tracing Back
t = | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
 | 00 | 00 | 10 | 01 | 10 | 11 | 11 | 01 | 00 | 10 | 01 | 10 | 01 | 00 | 00 | 10 | 01 | 00

## Slide 59: Coding Gain
Transmission voltages (signal to noise ratio SNR 20 dB).
No errors.

## Slide 60: Coding Gain
Transmission voltages with Gaussian noise (SNR 6dB)
bit error rate (BER) of about 0.235%

## Slide 61: Coding Gain
convolutional coding with Viterbi decoding can achieve a BER of less than 1 x 10-7 at the same SNR, 6 dB
r = ½, K = 3
Use 5db less power to achieve 1 x 10-7 BER than without coding
Coding uses twice as much (3dB) bandwidth
Coding gain: 5dB-3dB = 2dB less energy

## Slide 62: Viterbi decoder hardware

## Slide 63: Inside the ACS ("secret sauce" of Viterbi)

## Slide 64: Cool Viterbi Example
From Keith CHugg, USC, March 2017
Best insight-building discussion I have seen.
Objective: drive west to east coast of US
<750 mi/day
Figure of merit = distance (low score wins)
Array of 8 columns of 4 rows/states/nodes each
  like 8 consecutive symbols

## Slide 65: 4 cities to choose from each day

## Slide 66: problem: lots of potential paths

## Slide 67: Missing links make it a bit easier
If we were transmitting symbols from 2-sample states, we would have four possible states at each sample point in time, but we would also be able to go from any state to any other.
No real loss of generality in this example.
As with solving any complex problem, consider divide-and-conquer.
For each Day 2 node, what was the shortest distance from an available Day 1 node?

## Slide 68: Start w/ day 2 -- shortest paths to get there

## Slide 69: keep pruning

## Slide 70: second pruning -- total paths to 3rd column

## Slide 71: result

## Slide 72: Conclusion so far
Have eliminated 3 of 4 starting states
Have eliminated 2 of 4 2nd states, 3rd state, 4th states
Still show 4 possible destinations
  can pick the winner among these 4
Key is to eliminate long paths step by step
Note this model lets us start anywhere on west coast and end anywhere on east. If we constrain these endpoints, then we have only 6 sets of states in between.

## Slide 73: Lookback
Identified shortest path to ANY state (City) on E Coast
Go backward to reconstruct the route and the cumulative distance
Eliminate options as early as possible
Store the winners as you go to facilitate traceback at end

## Slide 74: How about genetic sequencing?
... or handwriting character recognition?
... or speech recognition?

## Slide 75: HMM : Viterbi algorithm -­ - example
Sources:
For the theory, see Durbin et al (1998);;
For the example, see Borodovsky & Ekisheva (2006), pp 80-­81
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
Simple Hidden Markhov Model comprises 2 states, H (high GC content) and L (low GC content).
The model can find a region of coding (H) DNA from a given sequence.

## Slide 76: HMM : Viterbi algorithm -­
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.5
0.6
0.4
Consider sequence S= GGCACTGAA
Several paths through the hidden states (H and L) lead to the given sequence S.
Example: P = LLHHHHLLL
The probability of the HMM to produce sequence S through the path P is: p = pL(0) * pL(G) * pLL * pL(G) * pLH * pH(C) * ...
= 0.5 * 0.2 * 0.6 * 0.2 * 0.4 * 0.3 * ...
= ...

## Slide 77: Where have we seen A,T,G,C before?

## Slide 78: HMM : Viterbi algorithm -­
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
GGCACTGAA
Several paths through the hidden states (H and L) lead to the given sequence, but not with equal probability.
The Viterbi algorithm = dynamic programming that computes the most probable path. Similar to the dynamic programs used to align 2 sequences (i.e. Needleman-­Wunsch)
Source: Borodovsky & Ekisheva, 2006

## Slide 79: HMM : Viterbi algorithm -
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
G G C A C T G A A
Viterbi algorithm: principle
The probability of the most probable path ending in state k with observation "i" is
probability to observe element i in state l
probability of the most probable path ending at position x-­1 in state k with element j
probability of the transition from state l to state k

## Slide 80: HMM : Viterbi algorithm -
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
G G C A C T G A A
Viterbi algorithm: principle
The probability of the most probable path ending in state k with observation "i" is
Here, the probability of the most probable path ending in state H with observation "A" at the 4th position is:
We can thus compute recursively (from the first to the last element of our sequence) the probability of the most probable path.

## Slide 81: HMM : Viterbi algorithm -
Start
H | 
A | -­2.322
C | -­1.737
G | -­1.737
T | -­2.322
L | 
A | -­1.737
C | -­2.322
G | -­2.322
T | -­1.737
-­1
-­1
-­1
-­1.322
-­1
-­0.737
Remark: convenient to use the log of the probabilities, rather than the probabilities themselves. This allows us to compute sums instead of products, which is more efficient and accurate.
We used here log2(p). (This is also used in LDPC.)
Can do log lookup table for speed or precompute once.

## Slide 82: HMM : Viterbi algorithm -
Start
H | 
A | -­2.322
C | -­1.737
G | -­1.737
T | -­2.322
L | 
A | -­1.737
C | -­2.322
G | -­2.322
T | -­1.737
-­1
-­1
-­1
-­1.322
-­1
GGCACTGAA
pH(G,1) = -­1 -­1.737 = -­2.737
pL(G,1) = -­1 -­2.322 = -­3.322
Probability (in log2) that G at the first position was emitted by state H
Probability (in log2) that G at the first position was emitted by state L
-­0.737

## Slide 83: HMM : Viterbi algorithm
Start
H | 
A | -­2.322
C | -­1.737
G | -­1.737
T | -­2.322
L | 
A | -­1.737
C | -­2.322
G | -­2.322
T | -­1.737
-­1
-­1
-­1
-­1.322
-­1
GGCACTGAA
pH(G,2) = -­1.737 + max (pH(G,1)+pHH, pL(G,1)+pLH)
= -­1.737 + max (-­2.737 -­1 , -­3.322 -­1.322)
= -­5.474 (obtained from pH(G,1))
pL(G,2) = -­2.322 + max (pH(G,1)+pHL, pL(G,1)+pLL)
= -­2.322 + max (-­2.737 -­1.322 , -­3.322 -­0.737)
= -­6.059 (obtained from pH(G,1))
Probability (log2) that G at the 2nd position was emitted by state H
Probability (log2) that G at the 2nd position was emitted by state L
-­0.737

## Slide 84: HMM : Viterbi algorithm
Start
H | 
A | -­2.322
C | -­1.737
G | -­1.737
T | -­2.322
L | 
A | -­1.737
C | -­2.322
G | -­2.322
T | -­1.737
-­1
-­1
-­1
-­1.322
-­1
GGCACTGAA
G
G
C
A
C
T
G
A
A
H
-­2.73
-­5.47
-­8.21
-­11.53
-­14.01
...
-­25.65
-­0.737
L -­3.32 -­6.06 -­8.79 -­10.94 -­14.01 ... -­24.49
We then compute iteratively the probabilities pH(i,x) and pL(i,x) that nucleotide i at position x was emitted by state H or L, respectively. The highest probability obtained for the nucleotide at the last position is the probability of the most probable path. This path can be retrieved by back-­tracking.

## Slide 85: HMM : Viterbi algorithm -
Start
H | 
A | -­2.322
C | -­1.737
G | -­1.737
T | -­2.322
L | 
A | -­1.737
C | -­2.322
G | -­2.322
T | -­1.737
-­1
-­1
-­1
-­1.322
-­1
GGCACTGAA
G
G
C
A
C
T
H
-­2.73
-­5.47
-­8.21
-­11.53
-­14.01
...
L
-­3.32
-­6.06
-­8.79
-­10.94
-­14.01
...
-­24.49
back-­tracking
(= finding the path which corresponds to the highest probability, -­24.49)
G A A
-­25.65
HHHLLLLLL
The most probable path is:
Its probability is 2-­24.49 = 4.25E-­8 (remember that we used log2(p))
-­0.737

## Slide 86: HMM : Forward algorithm -­
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.5
0.6
0.4
Consider now the sequence S= GGCA
What is the probability P(S) that this sequence S was generated by the HMM model?
This probability P(S) is given by the sum of the probabilities pi(S) of each possible path that produces this sequence.
The probability P(S) can be computed by dynamical programming using either the so-­called Forward or the Backward algorithm.

## Slide 87: HMM : Forward algorithm -
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
Consider now the sequence S= GGCA
Forward algorithm
 | Start | G | G | C | A
H | 0 | 0.5*0.3=0.15 |  |  | 
L | 0 | 0.5*0.2=0.1 |  |  | 

## Slide 88: HMM : Forward algorithm -­
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
Consider now the sequence S= GGCA
 | Start | G |  | G |  | C | A
H | 0 | 0.5*0.3=0.15 |  | 0.15*0.5*0.3 + 0.1*0.4*0.3=0.0345 |  |  | 
L | 0 | 0.5*0.2=0.1 |  |  |  |  | 

## Slide 89: HMM : Forward algorithm -­
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
Consider now the sequence S= GGCA
 | Start | G | G | C | A
H | 0 | 0.5*0.3=0.15 | 0.15*0.5*0.3 + 0.1*0.4*0.3=0.0345 |  | 
L | 0 | 0.5*0.2=0.1 | 0.1*0.6*0.2 + 0.15*0.5*0.2=0.027 |  | 

## Slide 90: HMM : Forward algorithm -­
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.4
0.5
0.6
Consider now the sequence S= GGCA
 | Start | G | G |  | C |  | A
H | 0 | 0.5*0.3=0.15 | 0.15*0.5*0.3 + 0.1*0.4*0.3=0.0345 |  |  | ... + ... | 
L | 0 | 0.5*0.2=0.1 | 0.1*0.6*0.2 + 0.15*0.5*0.2=0.027 |  |  | ... + ... | 

## Slide 92: HMM : Forward algorithm -
Start
H | 
A | 0.2
C | 0.3
G | 0.3
T | 0.2
L | 
A | 0.3
C | 0.2
G | 0.2
T | 0.3
0.5
0.5
0.5
0.5
0.6
0.4
The probability that sequence S="GGCA" was generated by the HMM model is PHMM(S) = 0.0038432.
To assess the significance of this value, we have to compare it to the probability that sequence S was generated by the background model (i.e. by chance).
Ex: If all nucleotides have the same probability, pbg=0.25;; the probability to observe S by
bg
chance is: Pbg(S) = p 4 = 0.254 = 0.00396.

## Slide 93: Medical Disclaimer
Thus, for this particular example, it is likely that the sequence S does not match the HMM model (Pbg > PHMM).
NB: Note that this model is very simple and does not reflect any biological motif. If fact both states H and L are characterized by probabilities close to the background probabilities, which makes the model not realistic and not suitable to detect specific motifs.

## Slide 94
Summary -- Viterbi algorithm:
computes the most probable path (and its probability)
requires knowledge of the parameters of the HMM model and a particular output sequence
finds the state sequence that most likely generated that output sequence
finds a minimum Hamming distance over all possible state sequences
In sequence analysis, this method can be used for example to predict coding vs non-­coding sequences.
Often many state sequences can produce the same output sequence, but with different probabilities. One can calculate the probability for the HMM model to generate that output sequence by summing over all possible state sequences.
In sequence analysis, this method can predict the probability that a particular DNA region matches the HMM motif (i.e., was emitted by the HMM model). A HMM motif can represent a TF binding site for example.

## Slide 95
Remarks
To create a HMM model (i.e. find the most likely set of state transition and output probabilities of each state), we need a set of (training) sequences, that does not need to be aligned.
No tractable algorithm is known for solving this problem exactly, but a local maximum likelihood can be derived efficiently using the Baum-­Welch algorithm or the Baldi-­Chauvin algorithm. The Baum-­Welch algorithm is an example of a forward-­backward algorithm, and is a special case of the Expectation-­maximization algorithm.
For more details: see Durbin et al (1998)
HMMER
The HUMMER3 package contains a set of programs (developed by S. Eddy) to build HMM models (from a set of aligned sequences) and to use HMM models (to align sequences or to find sequences in databases). These programs are available at the Mobyle plateform (http://mobyle.pasteur.fr/cgi-­bin/MobylePortal/portal.py)

## Slide 96: References (from Fleming)
Some Books about Forward Error Correction
S. Lin and D. J. Costello, Error Control Coding. Englewood Cliffs, NJ: Prentice Hall, 1982.
A. M. Michelson and A. H. Levesque, Error Control Techniques for Digital Communication. New York: John Wiley & Sons, 1985.
W. W. Peterson and E. J. Weldon, Jr., Error Correcting Codes, 2 nd ed. Cambridge, MA: The MIT Press, 1972.
V. Pless, Introduction to the Theory of Error-Correcting Codes, 3rd ed. New York: John Wiley & Sons, 1998.
C. Schlegel and L. Perez, Trellis Coding. Piscataway, NJ: IEEE Press, 1997
S. B. Wicker, Error Control Systems for Digital Communication and Storage . Englewood Cliffs, NJ: Prentice Hall, 1995.

## Slide 97: More References (from Fleming)
Some Papers about Convolutional Coding with Viterbi Decoding
For those interested in VLSI implementations of the Viterbi algorithm, I recommend the following paper and the papers to which it refers (and so on):
Lin, Ming-Bo, "New Path History Management Circuits for Viterbi Decoders," IEEE Transactions on Communications, vol. 48, October, 2000, pp. 1605-1608.
Other papers are:
G. D. Forney, Jr., "Convolutional Codes II: Maximum-Likelihood Decoding," Information Control, vol. 25, June, 1974, pp. 222-226.
K. S. Gilhousen et. al., "Coding Systems Study for High Data Rate Telemetry Links," Final Contract Report, N71-27786, Contract No. NAS2-6024, Linkabit Corporation, La Jolla, CA, 1971.
J. A. Heller and I. M. Jacobs, Viterbi Decoding for Satellite and Space Communications," IEEE Transactions on Communication Technology, vol. COM-19, October, 1971, pp. 835-848.
K. J. Larsen, "Short Convolutional Codes with Maximal Free Distance for Rates 1/2, 1/3, and 1/4," IEEE Transactions on Information Theory, vol. IT-19, May, 1973, pp. 371-372.
J. P. Odenwalder, "Optimum Decoding of Convolutional Codes," Ph. D. Dissertation, Department of Systems Sciences, School of Engineering and Applied Sciences, University of California at Los Angeles, 1970.
A. J. Viterbi, "Error Bounds for Convolutional Codes and an Asymptotically Optimum Decoding Algorithm," IEEE Transactions on Information Theory , vol. IT-13, April, 1967, pp. 260-269.